## Slide 1: Title IMPROVING IMAGING BY USING GENETIC ALGORITHMS TO FIND ARBITRARY PROFILES OF BESSEL BEAM LASER by Leon Hunter Project Advisors Dr. Tomasz Smolinski Dr. Thomas Planchon

## Slide 2: Overview
Background
  Adaptive optics
  Active optics
  Laser Shape
Goal
  Develop Genetic Algorithm (GA)
  Interface GA with software (LabVIEW)
  Improve result
Approach
  Hardware
  Software

## Slide 3: Background; Adaptive Optics
Process to enhance the performance of an optical system
  Reduces effect of wave front distortions using active optic
Active optics is an optical instrument with an adjustable reflective component; i.e. – spatial light modulator (SLM)
  actively shapes reflective surface to prevent deformation due to external influences.

## Slide 4: Background; Laser Shape
Naturally, the shape of laser follows Gaussian function. However, there is interest to use Bessel-shaped beams to improve measuring techniques.
  Gaussian: stays bounded over propagation range, then diverges
  Bessel: Ideally diffraction-free and do not diverge when propagating
Notice the information-rich areas in the images below
Notes: The point spread function (PSF) describes the response of an imaging system to a point source or point object. - how well you can see two nearby objects before they appear to be one object

## Slide 5: Goal; Develop Genetic Algorithm
Create basic structure of GA.
  Components of Genetic Algorithms include parents1, reproduction2, offspring3, and selection4.
    1. Parents - contain properties (DNA) to be reproduced and passed to offspring who may or may not survive depending on fitness for environment.
    2. Reproduction – process of parents’ genetic information being copied, mixed, and mutated.
    3. Offspring - resulting entities whose properties are yielded by reproduction
    4. Selection - actions to decide which offspring is most suited for parenting.
**Note: Evolution of the contending solution(s) occurs over many generations.
Notes: • Optimization of active optics controlled by genetic algorithms
• Genetic algorithms - type of optimization algorithm that grades potential solutions based on fitness and ability to survive in environment.
• Fitness function - the environment entities are being tested against.

## Slide 6
Create basic structure of GA.
  Components of Genetic Algorithms include parents1, reproduction2, offspring3, and selection4.
    1. Parents - contain properties (DNA) to be reproduced and passed to offspring who may or may not survive depending on fitness for environment.
    2. Reproduction – process of parents’ genetic information being copied, mixed, and mutated.
    3. Offspring - resulting entities whose properties are yielded by reproduction
    4. Selection - actions to decide which offspring is most suited for parenting.
10 different phase functions j(x,y) - Each phase function (parent) will be sent to SLM

## Slide 7: Goal; Interface Algorithm to SLM
Control spatial light modulator (SLM) used for shaping profile of laser beam
Measure result of shaping with 2D camera.
Notes: Spatial light modular – device used to modulate amplitude, phase, or polarization of light waves in space and time.
LED, series of crystals that orient themselves at an angle depending on voltage that is put through
Can be programmed to change the index of an image
Values of index within set S = { x ∈ Z : x ≤ 216 }

## Slide 8: Goal; Improve Results
Improve Bessel beam by finding new (unknown) profiles. (Hence use of learning optimization method)
  Improve GA by changing fitness function to optimize from one camera image to several (three to four) images taken at different planes.
Add additional parameters to fitness function.
Notes: The convergence and stability of the GA will then be investigated using optimization on several criteria
(laser size, profile similarity between planes, maximum of secondary peaks on the camera)
instead of a single criterion for optimization

## Slide 9: Approach; Hardware
Spatial light modulator – device used to modulate amplitude, phase, or polarization of light waves in space and time.
  LCD with crystals capable of orienting themselves at an angle signaled by voltage.
  Can be programmed to change index of an image
  Values of index within set { x ∈ Z : 0 ≤ x ≤ 216 }
Notes: Device to be manipulated by algorithm

## Slide 10: Approach; Software
LabVIEW - unified environment eliminates time otherwise used to build expertise in a variety of tools to accomplish your goal.
Suggested MatLab toolboxes for EAs
  Global Optimization Toolbox ($200.00)
  Statistics Toolbox ($200.00)
Suggested Python modules for EAs
  Deap.py - Distributed Evolutionary Algorithms (FREE)
  inspyred.py (FREE)
Notes: Python would require some hacking to get it to work
  In addition to this, it's likely that MatLab will be a better option because it is typically:
  more reliable, deterministic, and easily interfaced with LabVIEW

## Slide 11: Future Work
Apply solution to various fields of science who are faced with similar issues that can be solved by correcting wave front distortions.
Notes: i.e. - hydrodynamics, acoustics

## Slide 12: Thank you!
Questions?